## Slide 1: uNit 1 –Introduction to µI
Computing Systems

## Slide 2: From voltage to logic computing
Font:hispantv.com
Font:lg.com
Font:iRobot.es
Font:Lenovo.com
Font:App SimulIDE
...1101000110011
How is it possible?

## Slide 3: To sum up the starting point
Font:ebay.es
Font:Farnell.com
Resistor
Capacitor
Diode
Transistor; History: BJT and Mosfet
Coil
Tube

## Slide 4: To be voltatge or not to be voltage
Humans ned fingers to count
Humans have twenty fingers
Decimal is a positional system
Font:radiocampusparis.org
vs
Computers ned voltatge to count
Bi stands for two símbols 0 and 1
Binary is a positional system

## Slide 5: Voltatge to logic: GATES
BUFFER
NOT
AND
NAND
OR
NOR
XOR
XNOR
Font:hyperphysics.phy-astr.gsu.edu/

## Slide 6: NAND GATE
Font:hyperphysics.phy-astr.gsu.edu/
Font:wikipedia

## Slide 7: NOR GATE
Font:hyperphysics.phy-astr.gsu.edu/

## Slide 8: EXCLUSIVE OR GATE (XOR)
Font:hyperphysics.phy-astr.gsu.edu/
WITH NAND
EXCLUSIVE NOR GATE (XNOR)

## Slide 9: Flip Flop
Q | D | Qt+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Font:hispavila.com
CLOCK
Font:farnell.com
Has memory!

## Slide 10: Adder
112
112
+
______
1102
102
112
+
______
1012
A1 A0
B1 B0
S2 S1 S0
+
______
02+ 02 = 02
12+ 02 = 12
12+ 12 = 02
Overflow!!!
Carry one
A
B
S
2
2
3

## Slide 11: Multiplier
A
B
C
2
2
4

## Slide 12: Multiplexer & Demultiplexer
A | B | q
0 | 0 | d[0]
0 | 1 | d[1]
1 | 0 | d[2]
1 | 1 | d[3]
A | B | Y0 | Y1 | Y2 | Y3
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 13: State machine
Flip-flops has memory in a sequentially Systems.
Combinational Systems can create logical funcions.
Clocks and counters fix the states and sequency.
Sequences of states
dependent on a set of
input variables
Algorithms
Font:allaboutcircuits.com

## Slide 14: Dinamic Random Acces Memory
DRAM is an array designed for density.
Address neds n bits; n/2 for rows and n/2 for columns
Signals to control columns and rows CAS ans RAS.
Signals to enable write or read and data out or in.
Signal from clock.
Can’t hold data without power.
A0
A1
A2
A3
MAIN
MEMORY

## Slide 15: Static RAM Memory
4 transistors per bit and 2 more per port.
Does not need to be refresh but voltatge must be applied.
Designed for velocity.
What the diference beetwen RAM and SRAM

## Slide 16: Flash Memory
Acces sequentially.
Hold data without power.
Made with NAND gates.
One transistor per bit.
Data has to be erased in entire blocs but in one flash!
Font:wikipedia

## Slide 17: Architecture Von Neumann
A System BUS combining the functions of a data bus, an address bus, and a control bus.
Principal Memory is connected to a Control Process Unit and I/O through a System BUS.
A simple CPU consists of a Control Unit and an Arithmetic Logic Unit.
CU can be a state machine or it can be programed.
Test it!

## Slide 18: Computing System in layers
Software is programmed with human-friendly code.
The Compiler or interpreter transforms human-friendly code into binary code that represent data and instructions.
An instruction set are the instructions that the CPU can execute to do his work. It can be software or low level hardware control also called Firmware.
If the software can change, how does the CPU know
what to do when the system is turned on?
Font:uc university

## Slide 19: CISC vs RISC
CISC (Complex Instruction Set Computing)
  Reduce “instructions/program”.
  Tends to increase clock period.
  Easy for programmers.
RISC (Reduced Instruction Set Computing)
  Improve “cycles/instruction” with many single-cycle instructions
  Increases “instruction/program”, but hopefully not as much
  Help from smart compiler.
  Perhaps improve clock cycle time (seconds/cycle) via aggressive implementation allowed by simpler instructions.
Assembly is any low-level programming language in which there is a very strong correspondence between the instructions in the language and the architecture's
machine code instructions.
ASM
Today’s ISAs are actually targeted to one language. C programming language is very low level.
C
Object Code
Machine Language
COMPILER
ASSEMBLER

## Slide 20: Basic Input Output System (BIOS)
Originally the BIOS is a little firmware stored in a non volatile read only memory (ROM). The modern BIOS contents are stored on flash memory.
The user can interact and change some parameters that are hold while the battery has power.
The modern BIOS contents are stored on flash memory.
To performance a system check.
To find loader to init a boot.
Font:tecnologia-informatica.com
PROM→Progamable ROM only once.
EPROM→Erasable PROM all cells with ultraviolet light.
EEPROM→Electrically EPROM only bytes addressed are updated.

## Slide 21: The Bootloader
Program is a list of instructions.
Loader is a program routine that copies an executable program into main memory for execution.
The assembler gives the object code.
[BITS 16]; It works with 16 bits
[ORG 0x7C00]; Source where the bootloader is loaded into RAM
...
TIMES 510 - ($ - $$) db 0; Fill the rest of the sector with zeros
DW 0xAA55; Put this sign (little-endian 0x55AA) at the end of bootloader
Try to make a bootloader with NASM and QEMU
Hexadecimal
Code system with base 16
0123456789ABCDEF
Two Bytes
Hard Disck Drive
Font:macfixit.com.au

## Slide 22: Operative System
His Kernel is programed with low level language to interacts with the hardware.
OS Needs :
  A filesystem in a memory space as a tree.
  Sofware Daemon controller: i.e Init.d or System.d
  Daemons or processes with memory stack.
    Graphical server: i.e X11
    Desktop
  Applications
Linux, Why not?
Font:softzone.es

## Slide 23: To finish....
Thanks!